Pro Peak/ Makita Charger: This will charge all Makita drill batteries

Short Instructions:

First insert the battery.

Check that screen looks like this: Displaying Li-Ion, 3300mA, 14.4v;

If this is not the case then move to the long instructions.

LiIo CHARGE

C=3300mAh 14.4Vp

If so hold down the ‘Enter, Start Stop’ button (the one at the right-hand end, the 4th one from the left)  for two seconds. The screen will display ‘battery check’ and then start charging. The screen will look something like below (but with different numbers) when charging.

CHG   0.04 00002

LI+3.26A 15.331V

If this is not the case then move to the long instructions.

Long Instructions:

First insert the battery.

If the charging screen is not displaying the settings shown above then the correct charging settings need to be selected. You can do this as follows.

- First using the ‘Batt Type’ button (First from the left)  cycle through the settings until Li-ion is displayed.

- Next using the ‘Enter, Start Stop’ button  (4th from the left) select the ‘C=’ field (this will flash when selected) then increase or decrease the current using the ‘Inc’ or ‘Dec’ buttons (2nd and 3rd from the left) until 3300mAh is displayed.

- Using the ‘Enter, Start Stop’ button cycle to the next ‘Vp’ field. Again use the ‘Inc’ or ‘Dec’ buttons until 14.4Vp is displayed.

Now hold down the ‘Enter, Start Stop’ button for 2 seconds until ‘Battery Check’ is displayed and the screen looks similar to the next page but with

CHG   0.04 00002

LI+3.26A 15.331V